## Slide 1: Challenge 2 CS-EEE
Introduction to Feedback Control Systems

## Slide 2
Controller
System to be controlled
Manual
Automatic
Control is used to regulate or modify the behaviour of a system so it behaves in a specific desirable way over time
Examples of control systems are everywhere, from aerospace systems and wireless networks to bioengineering and traffic control
What is control
Notes: applies specific principles and methods to control dynamic systems so that they produce desired outcomes.

## Slide 3: Example: Vehicle speed control
car
driver
slope, wind, traffic…
actual velocity
accel.
brake
desired velocity

## Slide 4: Control Scheme
Open-Loop
car
-
Closed-Loop
feedback
Measurement
car
driver
slope, wind, traffic…
actual velocity
accel.
brake
desired velocity
desired velocity
accel.
brake
slope, wind, traffic…
actual velocity
Less accurate!

## Slide 5: Bang-Bang Control
Push back, against the direction of the error
  With constant action
Tracking error is
  is on
  is off
Another example: Household thermostat
Optimal for reaching the setpoint
Not very good for staying near it
How can you prevent the chattering?
Output: actual speed, temperature, etc.
Setpoint: desired speed, temperature, etc.

## Slide 6: The Bang-Bang Controller
Hysteresis switching
Error is
  is on
  is off
  with a small constant

## Slide 7: Proportional Control
The control is proportional to the error
  is the proportional(control) gain
Increasing gain approaches setpoint faster
Can lead to overshoot, and even instability
Steady-state offset (error) if used without an integral component
Increase

## Slide 8: PI Control
Using a Proportional-Integral (PI) Controller
  is the integral gain
Settles with zero steady-state error
May lead to a large overshoot as is going too fast as it approaches the setpoint – requires proper design approach ideally
Increase , fixed

## Slide 9: PID Control
using a Proportional-Integral (PI) Controller
  is the derivative gain
derivative action can counteract the tendency to overshoot or undershoot
But it’s vulnerable to noise !!
Increase , fixed and

## Slide 10: PID Control
Here is a schematic of an implementation of a typical PID controller.
In practice, we often use PI (e.g. driving a motor), or PD (e.g. balancing two-wheel vehicle), and NOT all three terms.

## Slide 11: PWM control
PWM module
output
PID output
PWM output

## Slide 12: Concluding remarks
Good behavior depends on good tuning!!
The P-action is introduced to increase the speed of the response. Exaggerated P-action results in oscillation.
The I-action is introduced to obtain zero steady-state error.
The D-action is introduced for damping purposes. The disadvantage is the sensitivity to the noise.
Although a cut-and-try design may work OK, for best performance a full design, based on fundamental principles, is needed.

## Slide 13: Integration and differentiation in Arduino
Numerical integration
  provided sufficiently small – needs the loop time to be measured and/or regulated
Numerical differentiation

## Slide 14: References
https://uk.mathworks.com/videos/series/understanding-pid-control.html
PID tuning
Common tunning methods:
Ziegler-Nichols method
Trial-and-error manual tuning

## Slide 15: References
Ziegler-Nichols method

## Slide 16: References
Trial-and-error manual tuning